## Slide 1
Flow Event Telemetry on Programmable Data Plane
Yu Zhou
Chen Sun, Hongqiang Harry Liu, Rui Miao, Shi Bai, Bo Li, Zhilong Zheng, Lingjun Zhu,
Zhen Shen, Yongqing Xi, Pengcheng Zhang, Dennis Cai, Ming Zhang, Mingwei Xu
E6636BC20180234D78A0072836F0B330A2B9B20F15EA8B80AFD98931B16E2BB62B43B638616EAB0F223927083846ADEB9C1921FA11D03BD11BBFC2EC7E7E1BDA24F933AD172394E7F41D284767024E87EED2EBE67302D1E708EAF19A11202C38DD86259E4E3

## Slide 2: Increasing SLA Requirements for Network Performance
Stable and lower latency
Cloud Gaming
Algorithmic Stock Trading
Block Storage Service
Higher throughput and lower loss
Cloud Network
Wide-Area Network
Access Network

## Slide 3: Network Performance Anomalies Violate SLA
Satisfactory network performance
Chart: 
Unsatisfactory network performance
Cloud Network
Wide-Area Network
Access Network
Network Performance
Anomaly (NPA)

## Slide 4: NPA is Wide-Spread in Production Networks
Chart: 
| Long tail latency | Bandwidth loss | Packet timeout
Network | 14 | 3 | 85
Server | 10 | 7 | 80
Resource provisioning | 1 | 1 | 8
Power | 0 | 1 | 10
Attack | 0 | 1 | 1
Network accounts for 46% application performance problems

## Slide 5: NPA Mitigation Lifecycle in Production Networks
NPA location occupies ~90% of the entire NPA mitigation lifecycle
Chart: Mitigation Lifecycle for NPA cases
10 Minutes
1 Hour
0.7 Day
Who to blame
    Network? Server?
What kind of NPA
Congestion? Drop?
Where NPA happens
Edge? Core?
NPA Location

## Slide 6: The Key Capability for NPA Location
flows
events
e.g. 2 The failed link drops
five customers’ packets
e.g. 1 Customer A’s traffic experienced congestion
Key capability for
NPA location
IP Address
Protocol
Transport Port
Congestion
Path Change
Packet Pause
Packet Drop
Virtual Net ID

## Slide 7: Problems of Existing Solutions
Mgmt Plane
Data Plane
flows
events
Blackbox
Counters
Syslogs
Small Overhead
Counter-based
Coarse data granularity
Event Only: Port 1 is down at 00:01
Flow Only: 1 packet of Flow 2 pass Port 1 at 00:01
Inaccurate Coorelation: Whether is Flow 2’s timeout caused by Port 1’s failure?

## Slide 8: Problems of Existing Solutions
Mgmt Plane
Data Plane
flows
events
Blackbox
Counters
Syslogs
Small Overhead
Gray-box
Large Overhead
flows
events
Packet Telemetry
Counter-based
Packets
Metadatas
Coarse data granularity
Fine data granularity
Packet 1 belongs to Flow 3
Packet 1’s queuing delay is 10ms in Device 2
Flow 3 is congested in Device 2

## Slide 9: Problems of Existing Solutions
Mgmt Plane
Data Plane
flows
events
Blackbox
Counters
Syslogs
Small Overhead
Gray-box
Large Overhead
flows
events
Packet Telemetry
Counter-based
Packets
Metadatas
Coarse data granularity
Fine data granularity

## Slide 10: The Right Way of NPA Location
Mgmt Plane
Data Plane
flows
events
Blackbox
Counters
Syslogs
Coarse data granularity
Small Overhead
Gray-box
Large Overhead
Fine data granularity
flows
events
Packet Telemetry
Counter-based
Packets
Metadatas
Programmable
flows
events
flows
events
Small Overhead
Flow Events
Flow Event Telemetry

## Slide 11
Mgmt Plane
Data Plane
Flow Event Generation
Flow Event Storage
NetSeer: Flow Event Telemetry (FET) on Programmable Data Plane
Chart: NPA cases
Chart: NPA cases
Slow NPA mitigation
Rapid NPA mitigation
minutes
hours
seconds

## Slide 12: Design Challenges
#1: Coverage
Full event coverage
(inter-switch drops)
High scalability of
event trans. & process
High accuracy within ASIC memory
#2: Scalability
#3: Accuracy
Step 1
Event Packet Selection
Step 2
Event Deduplicat-ion
Step 3
Event
Extraction
and Batching
Step 4
False Positive Elimination and Pacing
100%
10%
0.5%
0.01%
0.01%
Switch ASIC
Switch CPU

## Slide 13: Challenge 1: Coverage
Flow Events
Intra-Switch
Drop
Inter-Switch
Drop
Congestion
Packet Drop
Path Change
Packet Pause
18% of all drop cases
41% of total drop location time
but…
Chart: Failure Location Time (minutes)
| ≤30 | 31-60 | 61-120 | 121-180 | >180
Pipeline drop | 51 | 6 | 5 | 3 | 4
MMU congestion | 8 | 0 | 1 | 0 | 1
Inter-switch drop | 11 | 0 | 3 | 1 | 5
Hardware failure | 11 | 0 | 1 | 0 | 0
Pipeline Aware
Pipeline Unaware

## Slide 14: Understanding Inter-Switch Drop
﻿Bad transceivers, bent fiber, decaying transmitters, …
Hard to Detect Drops
In Pipeline
Hard to Recover Flows
In Pipeline
Upstream
Port
Downstream
Port
Packet drops at the MAC layer and no pipeline visibility
1
0
1
1
1
0
1
0
FCS Error

## Slide 15: Inter-Switch Coordination for Inter-Switch Drop Detection
Upstream Port
Downstream Port
11
12
12
13
14
14
③ Loss
detection
15
15
④ Loss
notification
11
12
13
14
15
11
10
16
...
Ring buffer
in the Upstream
Port
① Packet recording
② Packet numbering
⑤ Loss retrieval
Drop Detection
Flow Recovery

## Slide 16: Challenge 2: Scalability
Event Packets
Raw Packets
Drop
Event Packets
Congestion Event Packets
100Gbps
…
100Gbps
100Gbps
50,000 servers in one large DC
50,000 servers for monitoring
(unacceptable!!!)

## Slide 17: Redundancy Removal for Scalability
Step 1
Event Packet Selection
Step 2
Event Deduplicat-ion
Step 3
Event
Extraction
and Batching
Step 4
False Positive Elimination and Pacing
Event 1
Event 2
Event 3
Event 4
Event 5
E1
E2
E3
E4
E5
E1
E2
E3
E4
E5
100%
10%
0.5%
0.01%
0.01%
Remove redundant event packets
Remove redundant header/payload

## Slide 18: Event Deduplication with Zero False-Negative (FN)
Bloom Filter
0
1
0
1
0
0
1
…
…
hash
Hash collision
False Negative
Our Solution: Group Caching with Zero FN
Exact flow identifier | Cnt
1.1.1.1:1234 -> 2.2.2.2:5678 | 3
hash
② report
① replace
Effective deduplication (95%)
Zero false negative

## Slide 19: Event Extraction & Event Batching
Push
Pop
Recirculate by internal ports
IF event_num >= 50
  Report;
  Clone;
  Truncate;
ELSE
  Recirculate;
Event Stack
Event Extraction
Event Batching
Large transmission and processing overhead

## Slide 20: Challenge 3: Accuracy
Zero false negative
Potential false positive
Increased data volume
Inaccurate event severity
O(Mb) state
Limited actions
ASIC-CPU coordination to achieve zero false positive (FP)
Switch ASIC
Switch CPU
Best-Effort Partial Deduplication
False Positive Elimination
High speed
Massive memory
Flow events with FP
-95%
-7%

## Slide 21: Implementation and Overheads
NetSeer: The First FET-Based Monitoring System
  Tofino 32D ASIC, Netronome NFP-4000 SmartNIC
  ~ 12,000 Lines of Code: extension of Switch.P4
NetSeer is under deployment in Alibaba cloud networks
Network
packets
Flow
events
Ingress Pipeline
Egress Pipeline
MMU
Control
plane
Inter-switch packet numbering
and recording (ring buffer)
Inter-switch
drop detection
Pause
False positive elimination
Internal port
Path change
Congestion
Normal ports
Event compression
Tables lookup
Pipeline drop
MMU
congestion
drop
Pacing & reliable TCP-based report
Pipeline drop

## Slide 22: Implementation and Overheads
Hardware Resource Overheads
  SmartNIC: 5% additional memory
  Tofino ASIC
    40% stateful ALU usage, below 20% usage of other resources
Chart: 
| Exact xbar | Ternary xbar | Hash bits | SRAM | TCAM | VLIW actions | Stateful ALU | PHV
Switch.P4 | 0.3053 | 0.375 | 0.3343 | 0.3052 | 0.2812 | 0.3698 | 0.0833 | 0.83967
NetSeer | 0.1328 | 0.0152 | 0.081 | 0.1615 | 0.0208 | 0.0703 | 0.375 | 0.15014
Chart: 
| Exact xbar | Ternary xbar | Hash bits | SRAM | TCAM | VLIW actions | Stateful ALU | PHV
Event detection | 0.0404 | 0 | 0.0164 | 0.0219 | 0 | 0.0078 | 0.0417 | 0.059103
Inter-switch | 0.0247 | 0 | 0.0217 | 0.0667 | 0 | 0.0182 | 0.1458 | 0
Deduplication | 0.0371 | 0.0051 | 0.0187 | 0.0573 | 0.0035 | 0.0209 | 0.0625 | 0.066576
Batching | 0.0215 | 0.0038 | 0.0232 | 0.0146 | 0.0034 | 0.0182 | 0.125 | 0.024457

## Slide 23: Evaluation
    100Gbps
    switch links
  Monitoring Tools
    32x 25Gbps NFP-4000 smartNIC
    10 Tofino
    switches
NetSight
NetSeer
EverFlow
PingMesh
Sample 1:10, 1:100, 1:1000
NPA Location
Coverage & Accuracy
Scalability
61.3% ~ 99.9% location time reduction
100% event coverage without false positive
0.01% bandwidth overheads
Evaluation Highlights

## Slide 24: Evaluation: Real Case Study
NetSeer accelerates NPA location from minute-level to second-level
NetSeer reduces NPA location time by 61.3% to 99.9%
#1 Congestion due to unexpected volume
#2 ACL configuration error
#3 Silent drop due to parity error
#4 Routing error due to network update
#5 SSD firmware bug
Chart: Location Time (min)
| #1 | #2 | #3 | #4 | #5
w.o NetSeer | 162 | 73 | 442 | 113 | 284
w. NetSeer | 0.232 | 28.233 | 0.474 | 0.258 | 27.713

## Slide 25: Evaluation: Performance Benchmark
NetSeer monitors 100% flow events with full accuracy
NetSeer is scalable with 0.01% bandwidth overhead
NetSeer reconciles coverage, accuracy, and scalability

## Slide 26: Conclusion
flows
events
Small Overhead
Flow Events
Flow Event Telemetry
White-box
Fine data granularity
Flow event telemetry (FET)
  Flow events are key to NPA location
  Programmable data plane brings unprecedented opportunities for fine-grained and efficient monitoring
NetSeer: FET-based network monitor
  Inter-switch coordination for coverage
  ASIC-CPU coordination for scalability & accuracy
NetSeer is under deployment in Alibaba cloud